## Slide 1
Muon Collider 2011, Telluride, June 30, 2011
Acceleration Schemes for MC
Alex Bogacz
in collaboration with
Kevin Beard, Vasiliy Morozov
and
Yves Roblin
<number>

## Slide 2
Muon Collider 2011, Telluride, June 30, 2011
<number>
High/Medium/Low Emittance MC Schemes (1.5 TeV)
  Components, Layout, Transmission Efficiencies
  Cooling Performance ⇨ Accelerator acceptance
Acceleration Schemes (appropriate in various energy ranges)
  Linac and RLA
  FFAG Ring
  Fast Ramping Synchrotrons
High Transmission Acceleration scheme – initial beam dynamic choices
  Linac (0.4 – 1.5 GeV)
  RLAs (1.5 – 12.5 GeV) and (12.5 – 100 GeV)
  RCS Rings
Emerging Acceleration Scheme…
Overview

## Slide 3: Parameters of various MC options
 | Low ε (Johnson) | Med ε (Alexahin) | High ε (Palmer) | 
CM Energy | 1.5 | 1.5 | 1.5 | TeV
Luminosity | 2.7 | 1 | 1 | 1034cm2/s
Muons/bunch | 0.1 *10 | 1 | 2 | 1012
Ring circumference | 2.3 | 3 | 8.1 | km
β* = σz | 5 | 10 | 10 | mm
p/p (rms) | 1.0 | 0.1 | 0.1 | %
Ring depth | 35 | 13 | 135 | m
Muon survival | 30 | 4 | 7 | %
εT | 2.1 | 12 | 25 | π mm mrad
εL | 370,000 | 72,000 | 72,000 | π mm mrad
6/30/08
NuFact08, Valencia
Bob Palmer circa 2009
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 4
Muon Collider 2011, Telluride, June 30, 2011
<number>
HEMC – Phase space after cooling
Bob Palmer
εT | 25 | π mm mrad
εL | 72,000 | π mm mrad

## Slide 5: HEMC Scenario I (NF centric)
4.5
4.5
Berg/Palmer
Muon Collider 2011, Telluride, June 30, 2011
<number>
εT | 25 | π mm mrad
εL | 72,000 | π mm mrad
Notes: <number>

## Slide 6: HEMC Scenario II (Low Decay)
Berg/Palmer
Muon Collider 2011, Telluride, June 30, 2011
<number>
εT | 25 | π mm mrad
εL | 72,000 | π mm mrad
4.5
Notes: <number>

## Slide 7: Low Emittance MC Scenario
Rol Johnson
Muon Collider 2011, Telluride, June 30, 2011
<number>
εT | 2.1 | π mm mrad
εL | 370,000 | π mm mrad
Notes: <number>

## Slide 8: Linac + RLA
Moderate re-use of the linac (a few passes)
  Switchyard (single bend, horizontal)
  Individual energy return Arcs for recirculation
Increasing number of passes:
  Ramped linac quads
Reducing number of return Arcs:
  Use multi-pass(2) arcs based on combined function magnets
    Arcs now have larger aperture
    Simplifying switchyard
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 9: FFAG Rings
More passes through RF cavities (10+) – higher efficiency
  No switchyard (RLA)  single arc with large energy acceptance
Linear magnets to get large energy acceptance
  Linear non-scaling FFAG
Challenges
  Injection and extraction difficult (kickers: 15 cm radius, 0.1 T field)
  No synchrotron oscillations
  Amplitude dependent time of flight
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 10: Fast Ramping Synchrotron
Allows arbitrary number of passes (high efficiency)
Maintain beam synchronization with RF
Magnets ramped extremely fast
  Expensive power supplies (Eddy currents)
  Small apertures help to keep power down
  Beam not centered in magnets
High average bend field
  Ramping magnets have low field limit
  Hybrid lattice/magnets ⇨ SC magnets fixed field + warm magnets ramped
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 11: Acceleration with Improved Transmission
Muon Collider 2011, Telluride, June 30, 2011
<number>
Berg/Palmer
εT | 25 | π mm mrad
εL | 72,000 | π mm mrad
εT | 4,800 | π mm mrad
εL | 24,000 | π mm mrad
MC
192 =
NF

## Slide 12: Linac Cryo-module
Muon Collider 2011, Telluride, June 30, 2011
Linac cell (solenoid + 28 2-cell cavities), length: 22.75 meter
<number>
εT | 25 | π mm mrad
 2
0.9-2.5 Tesla solenoid
17 MV/m 201 MHz SRF

## Slide 13: Transit time effect – G4BL
Muon Collider 2011, Telluride, June 30, 2011
<number>
Kevin Beard
E = 400 MeV
= 3.7858

## Slide 14: 0.4-1.5 GeV Linac – Transverse Dynamics
227.5
0
5
0
5
0
Size_X[cm]
Size_Y[cm]
Ax_bet
Ay_bet
Ax_disp
Ay_disp
Muon Collider 2011, Telluride, June 30, 2011
<number>
= 25 mm mrad
2.5  beam envelope
10  cells
Transmission: 0.986

## Slide 15: Solenoid vs Quad focusing
Muon Collider 2011, Telluride, June 30, 2011
<number>
22.75
0
60
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
22.76
0
60
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y

## Slide 16: Longitudinal Matching
Muon Collider 2011, Telluride, June 30, 2011
70 deg. off-crest
<number>
longitudinal emittance: l lp z/mc) momentum spread: p/p bunch length: z | mm mm | 72 0.12 164
E = 400 MeV
= 3.7858
90 deg. off-crest
201 MHz, 17 MeV/m

## Slide 17: Longitudinal Dynamics
Energy [GeV]
Muon Collider 2011, Telluride, June 30, 2011
<number>
bucket area
initial stationary bucket gradually brought to 25 deg. off-crest
Synchrotron phase
0 = 3.79
 = 14.29
/0 = 3.7

## Slide 18
Muon Collider 2011, Telluride, June 30, 2011
<number>
0.4-1.5 GeV Linac – Transmission
Total loss: 6.4%
Muon decay: 5% loss
Transmission: 1.4% loss
MODELING A 0.4-1.5 GeV MUON LINAC, Beard at al

## Slide 19: ‘Dogbone’ RLA
allows both charges to traverse the Linac in the same direction (more uniform focusing profile)
better orbit separation at linac’s end ~ energy difference between consecutive passes (2E)
the droplets can be reduced in size according to the required energy
both charge signs can be made to follow a Figure-8 path (suppression of depolarization effects)
3 GeV
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 20
254.651
0
100
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
4-pass, 17-21 GeV
254.651
0
120
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
7-pass, 29-33 GeV
quad gradient
quad gradient
Muon Collider 2011, Telluride, June 30, 2011
<number>
Multi-pass ‘bisected’ linac Optics

## Slide 21
254.651
0
100
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
254.651
0
100
0
5
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
‘Fixed’ vs ‘Pulsed’ linac Optics (8-pass)
Pulsed
Fixed
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 22: Mirror-symmetric ‘Droplet’ Arc – Optics
130
0
15
0
3
-3
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
10 cells in
2 cells out
2 cells out
(out = in and out = -in , matched to the linacs)
transition
transition
E =5 GeV
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 23: ‘Dogbone’ RLA with 2-pass Arcs
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 24
60
300
C = 117.6 m
Two-pass Arc Layout
Simple closing of arc geometry when using similar super cells
1.2 / 2.4 GeV/c arc design used as an illustration can be scaled/optimized for higher energies preserving the factor of 2 momentum ratio of the two passes
Vasiliy Morozov
Droplet arc:
60 outward bend
300 inward bend
60 outward bend
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 25
Super-Cell Optics for P2/P1 = 2
P
2xP
Vasiliy Morozov
Each arc is composed of symmetric super cells consisting of linear combined-function magnets (each bend: 2.50)
= 600
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 26
‘Droplet’ Arc  Spreader/Recombiner
First few magnets of the super cell have dipole field component only, serving as Spreader/Recombiner
* Trajectories are shown to scale
Vasiliy Morozov
B | 1 .7 Tesla
G | 28 Tesla/m
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 27
A pair of 2-pass Arcs  Switchyard
Lower momentum arc is the most challenging because of the highest momentum ratio; have a solution but still plenty of room for optimization
* Trajectories are shown to scale
Vasiliy Morozov
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 28
Vertical Bypass Concept
3xP
4xP
Vasiliy Morozov
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 29
Advantages of New Arc Design
No need for a dedicated switchyard with spreader/recombiner incorporated into the arc design
Optimization of magnet bending angles in addition to quadrupole components allows for greater compactness and minimal orbit excursion (equal same-direction bends used as initial condition in the optimization)
Greater dynamic aperture and momentum acceptance expected with linear-field lattice
Simpler linear combined-function magnet design
Fully scalable Optics
MULTIPASS MUON RLA RETURN ARCS BASED ON LINEAR COMBINED-FUNCTION MAGNETS, Morozov et al
Muon Collider 2011, Telluride, June 30, 2011
<number>

## Slide 30: RLA s with multi-pass Arcs
Muon Collider 2011, Telluride, June 30, 2011
2.44 GeV/pass
1.5 GeV
10.3 GeV/pass
12.5 GeV
1.5-12.5 GeV RLA (4.5-pass)
12.5-100 GeV RLA (8.5-pass)
310 m linac (201 MHz)
960 m linac (402 MHz)
<number>

## Slide 31: Summary
Muon Collider 2011, Telluride, June 30, 2011
<number>
MC Acceleration Schemes (1.5 TeV)
  High//Low Emittance
  Cooling Performance ⇨ Accelerator acceptance
  Transmission Efficiencies
Longitudinal matching into a single pass Linac
‘High Transmission’ Acceleration scheme – initial beam dynamic choices
  Linac (0.4 – 1.5 GeV)
  RLAs (1.5 – 12.5 GeV) and (12.5 – 100 GeV)
  RCS Rings
Emerging Acceleration Scheme…

## Slide 32: Injection/Extraction Chicane
1.5 GeV
$Lc = 60 cm
$angH = 9 deg.
$BH = 10.2 kGauss
2.1 GeV
$Lc = 60 cm
$angV = 5 deg.
$BV = 4.7 kGauss
H
-H
V
H
-H
-V
3 cells
4 cells
30
0
30
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
FODO lattice:
900/1200 (h/v) betatron phase adv. per cell
Double achromat Optics





0.9 GeV
50 cm
1.7 m
Muon Collider 2011, Telluride, June 30, 2011
<number>